## Slide 1: Low-frequency acoustic analysis in Nunatsiavut
500 Hz - 0 Hz

## Slide 2: Identified calls
Upsweep (N Atl right, humpback, bowhead, sei)
Downsweep (Sei, Blue D)
Fin 20Hz
Fin 40Hz
Blue 9Hz
Minke pulse train
Banded (N Atl right, pinniped, bowhead)

## Slide 3: Parameters:
LTSA:
  Plot length: 1 hour
  End Hz: 500 Hz
  Brightness: 6 (adjust if necessary)
  Contrast: 250 (adjust if necessary)
Spectrogram:
  Plot length: 60 seconds
  End Hz: 200 Hz
  %Overlap: 90
  FFT length: 1000
  Same brightness/contrast as used for LTSA, minor adjustments okay.

## Slide 4: Fin whale
40 Hz pulses:
Duration: ≤1 second
Downsweep ranging from 80 ~ 40Hz
20 Hz calls:
Duration: ≤1 second
Pulse ranging from 30 ~ 10Hz (can have varying bandwidth)
Their calls are loud, around 190dB
They repeat every 10-40s and can last for hours.

## Slide 5: Fin whale
40 Hz call

## Slide 9: 20 Hz pulse

## Slide 13: Sei whale
Downsweep calls:
Duration: 1-4s
Downsweep ranging from: 100Hz ~ 30Hz
Upsweep calls:
Duration: >1s
Upsweep pulses ranging: >500Hz

## Slide 14
Downsweep ranges from 80 Hz to 30 Hz
Lasts about 3s

## Slide 19
?

## Slide 21: Minke whale
Pulse trains
Duration: 20 - 60 s
Peak frequency: 50 ~ 200 Hz
Pulse trains have fluctuating interpulse intervals

## Slide 24: Bryde’s whale
Be 7
Duration: 1-2.5 s
Frequency: 44 Hz
About 2-4 harmonics visible
Pulse bout
Duration: 0.5-1 s
Pulse bouts vary in length from 2-15 pulses
Downsweep frequency: 80 ~ 120 Hz
Interpulse interval: 1 s

## Slide 25
Be 7

## Slide 27
Bryde's whale pulse bout or minke whale pulse train?

## Slide 29: North Atlantic Right Whale
Most of these calls exist below 500 Hz with some vocalizations reaching 4000 Hz.
Up call
Duration: 2 s
This short “whoop” starts around 50Hz and ends around 450Hz.
Scream call
Duration: 0.5-3.0 s
These calls range in frequency from 400-3200 Hz
Gunshot call
Duration: 1 s
These quick, intense, gunshot-like sounds range in frequency from 0-1000 Hz
They function as a threat display to other males.

## Slide 30
Scream call (banded)
Up call

## Slide 31
Up call

## Slide 36: Blue Whale
North Atlantic A calls
Duration: 8 s
Constant frequency of around 20
North Atlantic B calls
Duration: 2-5 s
Downsweep with frequency ranging from 40-15Hz
Arch
Duration: 7 s
Call frequency range: 70-30 Hz (very variable)
Units are combined into phrases which are repeated to form a song.
North Atlantic blue whale songs were first described as consisting of a single tonal unit near 19Hz
Shal et al 2019: blue whale downsweeps range from 80-30Hz (D calls) duration: 1.8(0.6-4.1s)

## Slide 37
Arch

## Slide 38
North Atlantic A call followed by a B call

## Slide 42
B call

## Slide 47: Unidentified

## Slide 48
Seismic survey